## Slide 1: Putting railway hearing standards into perspective

## Slide 2
SEAFARERS | AVIATION | RAILWAY
International Labour Office | EASA (class 1) | UIMC (group A)
500, 1000, 2000, 3000 Hz 30dB unaided (better ear) 40 dB unaided (less good ear) | 500, 1000, 2000, 3000 Hz 35 dB (500, 1000, 2000 Hz) 50 dB (3000 Hz) Either ear seperatly | 500, 1000, 2000 Hz 40 dB at 500, 1000 Hz 45 dB at 2000 Hz (less good ear) Guideline
Pure tone audiometry Alternative assessment methods are acceptable Speech and whisper testing may be used for rapid practical assessment (3 meters) | Pure tone audiometry | Pure tone audiometery In doubt, a test in practice shall be given
Hearing aids acceptable if it has been confirmed that the individual will be capable of safely and effectively performing routine and emergency duties | Hearing aids allowed if if they provide optimal hearing function, are well tolerated and suitable for aviation purposes. | No hearing aids allowed

## Slide 3
SEAFARERS | AVIATION | RAILWAY
International Labour Office | EASA (class 1) | UIMC (group A)
500, 1000, 2000, 3000 Hz 30dB unaided (better ear) 40 dB unaided (less good ear) | 500, 1000, 2000, 3000 Hz 35 dB (500, 1000, 2000 Hz) 50 dB (3000 Hz) Either ear seperatly | 500, 1000, 2000 Hz 40 dB at 500, 1000 Hz 45 dB at 2000 Hz (less good ear)
Pure tone audiometry Alternative assessment methods are acceptable Speech and whisper testing may be used for rapid practical assessment (3 meters) | Pure tone audiometry | Pure tone audiometery In doubt, a test in practice shall be given
Hearing aids acceptable if it has been confirmed that the individual will be capable of safely and effectively performing routine and emergency duties | Hearing aids allowed if if they provide optimal hearing function, are well tolerated and suitable for aviation purposes. | No hearing aids allowed

## Slide 4
UIMC | Australia | USA
UIMC guidelines | National Standard for Health Assessment of Rail Safety Workers | FRA, 49 CFR §240.121 §242.117
500, 1000, 2000 Hz 40 dB at 500, 1000 Hz 45 dB at 2000 Hz (less good ear) | 500, 1000, 2000, 4000 Hz 40 dB (better ear) | 500, 1000, 2000 Hz 40 dB (better ear)
Pure tone audiometery In doubt, a test in practice shall be given | Pure tone audiometry Speech discrimination test | Pure tone audiometry Leaves the ability for further individual assessment
No hearing aids allowed | Hearing aids allowed – cochlear implant on individual basis | Hearing aids allowed

## Slide 5
Canada | Europe / UK | Netherlands
Railway Safety Act | EUR-Lex Directive 2007/59/EG Train Driving Licences and Certificates Regulations 2010 (TDLCR) + ORR medical guidance | Regeling spoorwegpersoneel 2011
500, 1000, 2000 Hz 40 dB (each ear) | 500, 1000, 2000 Hz 40 dB 500, 1000 Hz 45 dB 2000 Hz (less good ear) (guideline) | 1000, 2000, 4000 Hz Sum loss best ear > 80 dB = further evaluation Sum loss worse ear > 100 dB = further evaluation Sum loss best ear > 120 dB = unfit
Pure tone audiometry Practical test may allowed | Sufficient hearing, confirmed by an audiogram: hearing good enough to hold a phone conversation and to be able to hear warning sounds and radio messages | Pure tone audiometry
Hearing aids allowed | Hearing aids allowed in special cases | Hearing aids allowed

## Slide 6: Comparison
Pure-tone audiometry = cornerstone
Substantial differences exist in how hearing fitness is defined
Acceptance of hearing aids

## Slide 7: Conclusion
Are we measuring hearing loss or hearing performance?
Future standards may benefit from incorporating more functional measures of hearing ability.